## Slide 1: AAA Authentication
Console
Remote Access

## Slide 2: AAA Authentication?
Authentication, Authorization, and Accounting framework is used to manage the activity of the user to a network that it wants to access by authentication, authorization, and accounting mechanism.

## Slide 3: Configure a local user account on R1 and configure authenticate on the console and vty lines using local AAA.
1. Configure a username of admin1 with a secret password of admin1pa55.
- username admin1 secret admin1pa55
- aaa new-model
- aaa authentication login default local
- line con 0
- login authentication default
Check if login in console is working R1

## Slide 4: Configure a local user account on R1 and configure authenticate on the console and vty lines using local AAA.
2. Configure Local AAA Authentication for vty Lines on R1
- ip domain-name ccnasecurity.com
- crypto key generate rsa
- 1024
- aaa authentication login SSH-LOGIN local
- line vty 0 4
- login authentication SSH-LOGIN
- transport intput ssh
- end
Check if SSH is working in the PC

## Slide 5: Configure server-based AAA authentication using TACACS+.
Terminal Access Controller Access-Control System
1. Configure Server-Based AAA Authentication Using TACACS+ on R2.
- username admin2 secret admin2pa55
2. Verify the TACACS+ Server configuration.
- complete the information needed by the server
- client name: R2
- client IP: 192.168.2.1
- secret: tacacspa55
- server type: tacacs
- user setup (add users to access the router)

## Slide 6: Configure server-based AAA authentication using TACACS+.
3. Configure the TACACS+ server specifics on R2.
- tacacs-server host 192.168.2.5
- tacacs-server key tacacspa55
- aaa new-model
- aaa authentication login default group tacacs+ local
- line con 0
- login authentication default
Check if tacacs+ is working on console

## Slide 7: Configure server-based AAA authentication using RADIUS.
Remote Authentication Dial-In User Service
1. Configure Server-Based AAA Authentication Using RADIUS on R3
- username admin2 secret admin2pa55
2. Verify the Radius Server configuration.
- complete the information needed by the server
- client name: R2
- client IP: 192.168.3.1
- secret: tacacspa55
- server type: radius
- user setup (add users to access the router)

## Slide 8: Configure server-based AAA authentication using RADIUS.
3. Configure the Radius server specifics on R2.
- radius-server host 192.168.3.5
- radius-server key radiuspa55
- aaa new-model
- aaa authentication login default group radius local
- line con 0
- login authentication default
Check if radius is working on console