## Slide 1: ASA Firewall Setup
CISCO ASA Firewall Appliance

## Slide 2: What is a firewall?
A firewall is a network security device that monitors incoming and outgoing network traffic and permits or blocks data packets based on a set of security rules. Its purpose is to establish a barrier between your internal network and incoming traffic from external sources (such as the internet) in order to block malicious traffic like viruses and hackers.

## Slide 3: Types of Firewalls
Next-generation firewalls (NGFW) combine traditional firewall technology with additional functionality, such as encrypted traffic inspection, intrusion prevention systems, anti-virus, and more. Most notably, it includes deep packet inspection (DPI). While basic firewalls only look at packet headers, deep packet inspection examines the data within the packet itself, enabling users to more effectively identify, categorize, or stop packets with malicious data. Learn about Forcepoint NGFW here.
Proxy firewalls filter network traffic at the application level. Unlike basic firewalls, the proxy acts an intermediary between two end systems. The client must send a request to the firewall, where it is then evaluated against a set of security rules and then permitted or blocked. Most notably, proxy firewalls monitor traffic for layer 7 protocols such as HTTP and FTP, and use both stateful and deep packet inspection to detect malicious traffic.

## Slide 4: Types of Firewalls
Network address translation (NAT) firewalls allow multiple devices with independent network addresses to connect to the internet using a single IP address, keeping individual IP addresses hidden. As a result, attackers scanning a network for IP addresses can't capture specific details, providing greater security against attacks. NAT firewalls are similar to proxy firewalls in that they act as an intermediary between a group of computers and outside traffic.
Stateful multilayer inspection (SMLI) firewalls filter packets at the network, transport, and application layers, comparing them against known trusted packets. Like NGFW firewalls, SMLI also examine the entire packet and only allow them to pass if they pass each layer individually. These firewalls examine packets to determine the state of the communication (thus the name) to ensure all initiated communication is only taking place with trusted sources.

## Slide 5: Types of Firewalls
Packet-filtering Firewalls
Circuit-level Gateways
Application-level Gateways (Proxy Firewalls)
Stateful Multi-layer Inspection (SMLI) Firewalls
Next-generation Firewalls (NGFW)
Threat-focused NGFW
Network Address Translation (NAT) Firewalls
Cloud Firewalls
Unified Threat Management (UTM) Firewalls

## Slide 6: What is ASA 5505 Firewall
Adaptive Security Appliance (ASA)
The Cisco ASA 5505 is a full-featured firewall for small business, branch, and enterprise teleworker environments. It delivers high-performance firewall, SSL and IPsec VPN, and rich networking services in a modular, immediately operational appliance.
  Feature: Cisco ASA 5505; Security Plus
  IPS throughput 2: Up to 75 Mbps with AIP‑SSC-5
  Maximum 3DES/AES VPN Throughput 3: Up to 100 Mbps
  Stateful inspection throughput (maximum 1): Up to 150 Mbps
IPSec throughput is the amount of traffic that can pass through the firewall and the encrypted tunnel to your remote site. Most good firewalls use hardware encryption so IPSec numbers should approximate the overall throughput of your firewall.

## Slide 7: How to configure internet access on CISCO ASA 5505
SetUp the Firewall ASA
Initial Config
  1. Check for previous configuration
  2. Erase and Reload
  3. Enable command (no password, just press enter)
  4. Change hostname
  5. Enable password (put password)
Interface Configuration
Configure Gateway of ASA (OUTSIDE)
  int g1/1 (pointing to ISP)
  ip address and subnet mask
  nameif (name of outside network)
  security level 0
  no shut

## Slide 8: Here are a couple of examples of security levels:
Security level 0: This is the lowest security level there is on the ASA and by default it is assigned to the “outside” interface. Since there is no lower security level this means that traffic from the outside is unable to reach any of our interfaces unless we permit it within an access-list.
Security level 100: This is the highest security level on our ASA and by default this is assigned to the “inside” interface. Normally we use this for our “LAN”. Since this is the highest security level, by default it can reach all the other interfaces.
Security level 1 – 99: We can create any other security levels that we want, for example we can use security level 50 for our DMZ. This means that traffic is allowed from our inside network to the DMZ (security level 100 -> 50) and also from the DMZ to the outside (security level 50 -> 0). Traffic from the DMZ however can’t go to the inside (without an access-list) because traffic from security level 50 is not allowed to reach security level 100. You can create as many security levels as you want…

## Slide 9: How to configure internet access on CISCO ASA 5505
Configure Gateway of ASA (INSIDE)
  int g1/2 (pointing to LAN)
  ip address and subnet mask
  nameif (name of the inside network)
  security level 100
  no shut
You can verify the configuration
  show int ip brief
  show run

## Slide 10: How to configure internet access on CISCO ASA 5505
Creating DHCP server for LAN
  1. Creating the pool
  - dhcp address 192.168.1.10-192.168.1.20 inside
  2. Setup the DNS Server
  - dhcp dns 8.8.8.8
  3. Setup the Default Gateway of the LAN
  - dhcp option 3 ip 192.168.1.1 (default gateway)
  4. Enable the DHCP (insde)LAN
  - dhcp enable inside (to enable dhcp)

## Slide 11: How to configure internet access on CISCO ASA 5505
Configure the Default Route
  1. Enable default route (similar to static routing)
  - route outside 0.0.0.0 0.0.0.0 10.1.1.2
You can verify the configuration
  show int ip brief
  show run

## Slide 12: How to configure internet access on CISCO ASA 5505
Configure NAT
  1. Create Object groups - Objects are reusable components for use in your configuration. The Object Groups feature allows us to classify users, devices, or protocols into groups and apply those groups to access control lists (ACLs).
  - object network INSDE-NET
  - subnet 192.168.1.0 255.255.255.0
  2. Setup the NAT
  - nat (inside,outside)dynamic interface

## Slide 13: How to configure internet access on CISCO ASA 5505
Firewall Permission
  1. Create a class-map - The ASA uses class map to identify traffic, IP addresses, Layer 4 protocols, or application protocols.
  - class-map <inspection_default>
  2. Match the class-map to the default-inspection-traffic
  - match default-inspection-traffic
  3. Create a global policy
  - policy-map global_policy
  - class inspection_default
  - inspect icmp
  4. Apply the services to the traffic you are allowing
  - service-policy global_policy global

## Slide 14: How to configure internet access on CISCO ASA 5505
Adding Permission to ASA
  1. If you want to add permission, use the commands:
  - policy-map global_policy
  - class inspection_default
  - inspect <protocol>
  protocols:
  DNS
  HTTP
  FTP
  ICMP